## Slide 1: Artisan Mastery: Vegan Coffee Gelato
A Professional Formulation & Manufacturing Guide

## Slide 2: Small Scale Preparation (Home/Lab Test)
Step 1: Dry Blending: Mix Sugar, Guar Gum, and Gum Arabic to prevent clumping.
Step 2: Coffee Infusion: Steep Coffee Grounds and Instant Coffee in 122°F water for 5 minutes; strain.
Step 3: Mixing & Emulsification: Add Syrup and Sea Salt. At 140°F, incorporate Coconut Oil and Cashew Butter with a high-speed immersion blender for 2 minutes.
Step 4: Pasteurization & Aging: Heat to 185°F for 30 seconds. Cool and age at 40°F for 6–12 hours before churning.

## Slide 3: Industrial Manufacturing Process
Dispersion: Mix dry powders and syrups into 113°F water using a high-shear agitator.
Two-Stage Homogenization: Pass the hot mix through a homogenizer at 180/40 bar to ensure a microscopic fat emulsion.
Flash Cooling: Use a plate heat exchanger to drop the temperature to 40°F instantly.
Continuous Freezing: Churn with 25–35% overrun for a dense, premium texture.

## Slide 4: Flavor & Aromatic Profile
The Coffee Punch: A dark, vibrant profile reminiscent of a specialty Mocha or Long Black, unmasked by dairy fat.
The Cashew Undertone: Toasted nuttiness from the cashew base provides a creamy bridge.
Aromatic Experience: Intense roasted coffee aromatics balanced by nutty notes.

## Slide 5: Texture & Sensory Experience
Mouthfeel: Exceptionally smooth and "heavy" due to high solids from the cashew and syrup.
Melting Behavior: Slower than a sorbet but cleaner than heavy dairy; feels "warm" and velvety on the palate.
Visual Appeal: A deep, rich tan with a matte finish and premium artisanal "micro-dots" of coffee.

## Slide 6: Technical Specifications
Aging Time: 6–12 hours at 40°F.
Overrun Target: 25–35%.
Hardening Temperature: Core temperature of 0°F to -10°F.